## Slide 1
Presented by Marwan M. Alkhweldi
Co-authors Natalia A. Schmid and Matthew C. Valenti
Distributed Estimation of a Parametric Field
Using Sparse Noisy Data
This work was sponsored by the Ofﬁce of Naval Research under Award No. N00014-09-1-1189.

## Slide 2: Outline
Overview and Motivation
Assumptions
Problem Statement
Proposed Solution
Numerical Results
Summary

## Slide 3: Overview and Motivation
WSNs have been used for area monitoring, surveillance, target recognition and other inference problems since 1980s [1].
All designs and solutions are application oriented.
Various constraints were incorporated [2]. Performance of WSNs under the constraints was analyzed.
The task of distributed estimators was focused on estimating an unknown signal in the presence of channel noise [3].
We consider a more general estimation problem, where an object is characterized by a physical field, and formulate the problem of distributed field estimation from noisy measurements in a WSN.
[1] C. Y. Chong, S. P. Kumar, “Sensor Networks: Evolution, Opportunities, and Challenges” Proceeding of the IEEE, vol. 91, no. 8, pp. 1247-1256, 2003.
[2] A. Ribeiro, G. B. Giannakis, “Bandwidth-Constrained Distributed Estimation for Wireless Sensor Networks - Part I:Gaussian Case,” IEEE Trans. on Signal Processing, vol. 54, no. 3, pp. 1131-1143, 2006.
[3] J. Li, and G. AlRegib, “Distributed Estimation in Energy-Contrained Wireless Sensor Networks,” IEEE Trans. on Signal Processing, vol. 57, no. 10, pp. 3746-3758, 2009.

## Slide 4: Assumptions
Z1
Z2
.
ZK
Fusion Center
http://www.classictruckposters.com/wp-content/uploads/2011/03/dream-truck.png
A
Transmission Channel
Observation Model
The object generates
fumes that are modeled as
a Gaussian shaped field.

## Slide 5: Problem Statement
Given noisy quantized sensor observations at the Fusion Center,
the goal is to estimate the location of the target and the distribution
of its physical field.
Proposed Solution:
Signals received at the FC are independent but not i.i.d.
Since the unknown parameters are deterministic, we take the maximum likelihood (ML) approach.
Let be the log-likelihood function of the observations at the Fusion Center. Then the ML estimates solve:

## Slide 6: Proposed Solution
The log-likelihood function of is:
The necessary condition to find the maximum is:

## Slide 7: Iterative Solution
A. P. Dempster, N. M. Laird, and D. B. Rubin, “Maximum likelihood from incomplete data via the em algorithm," J. of the Royal Stat. Soc. Series B, vol. 39, no. 1, pp. 1-38, 1977.
Incomplete data:
Complete data: ,
where , and .
Mapping: .
where .
The complete data log-likelihood:

## Slide 8: E- and M- steps
Expectation Step:
Maximization Step:

## Slide 9: Experimental Set Up
Assume the area A is of size 8-by-8;
K sensors are randomly distributed over A;
M quantization levels;
SNR in observation channel is defined as:
SNR in transmission channel is defined as:

## Slide 10: Performance Measures
Target Localization
Shape Reconstruction

## Slide 11: Numerical Results
The simulated Gaussian field and squared difference between the original and reconstructed fields where

## Slide 12: EM - convergence
SNRo=SNRc=15dB.
Number of sensors K=20.

## Slide 13: Box-plot of Square Error
1000 Monte Carlo realizations.
SNRo=SNRc=15dB.

## Slide 14: Box-plot of Integrated Square Error
1000 Monte Carlo realizations.
SNRo=SNRc=15dB.
Number of quantization levels M=8

## Slide 15: Probability of Outliers
1000 Monte Carlo realizations.
SNRo=SNRc=15dB.
Number of quantization levels M=8.

## Slide 16: Effect of Quantization Levels
1000 Monte Carlo realizations.
SNRo=SNRc=15dB.
Number of sensors K=20.

## Slide 17: Summary
    An iterative linearized EM solution to distributed field estimation is presented and numerically evaluated.
    SNRo dominates SNRc in terms of its effect on the performance of the estimator.
    Increasing the number of sensors results in fewer outliers and thus in increased quality of the estimated values.
    At small number of sensors the EM algorithm produces a substantial number of outliers.
    More number of quantization levels makes the EM algorithm takes fewer iterations to converge.
    For large K, increasing the number of sensors does not have a notable effect on the performance of the algorithms.

## Slide 18: Contact Information
Natalia A. Schmid
e-mail: Natalia.Schmid@mail.wvu.edu
Marwan Alkhweldi
e-mail: malkhwel@mix.wvu.edu
Matthew C. Valenti
e-mail: Matthew.Valenti@mail.wvu.edu